## Slide 1: CIRCULAR ECONOMY
STRATEGIES, SUSTAINABLE
WASTEWATER
MANAGEMENT AND
RECYCLING
Presentation by: Engr. Oladele Fadipe FNSE, FNICE,
FINSafetyE, FINAR, MNIWE MGBCN

## Slide 2: INTRODUCTION
Over 3.6 billion people globally lack access to safely managed sanitation (WHO/UNICEF JMP, 2023). The result is untreated Wastewater entering drainage networks, open spaces, and water bodies.
A circular economy framework offers an alternative paradigm. Rather than viewing wastewater as an environmental liability, Our principles should reconceptualize it as a valuable bio-resource stream capable of generating:
markets,
carbon
Renewable biogas and electricity
Organic fertilizers and soil amendments
Water for irrigation or industrial reuse
Revenue through energy sales, compost credits, and circular business models
Government agencies such as; ministries of environment, water resources, municipalities, and public health regulators are essential to enabling this transition through supportive policy, investment, and enforcement.

## Slide 3: PROBLEM STATEMENT
Current Wastewater systems rely heavily on unsafely managed containment, uncontrolled dumping, and environmentally harmful disposal practices. These systems contribute to greenhouse gas emissions, groundwater contamination, and escalating health burdens in urban and peri-urban communities. The absence of resource recovery, results in significant economic losses, while poor regulatory enforcement deepens existing challenges. Without a structural shift, the pressure on public health and urban sanitation infrastructure will continue to intensify.

## Slide 4
Wastewater treatment is a critical process that removes contaminants from sewage and industrial effluents before they are released into the environment. It helps protect public health, prevents water pollution, and ensures the sustainable use of water resources

## Slide 5
WHY
Wastewater Treatment

## Slide 6: Prevention of Water Pollution
Wastewater contains organic matter, nutrients (nitrogen, phosphorus), and heavy metals that can degrade water quality.
Treatment plants remove pollutants before discharging water into rivers and oceans
.

## Slide 7: Protection of Public Health
Untreated sewage contains pathogens that can cause diseases such as cholera,
typhoid, and hepatitis.
Proper wastewater treatment reduces the risk of
waterborne diseases and ensures safe drinking water.

## Slide 8: Environmental Sustainability
Reduces eutrophication caused by excessive nutrient discharge.
  Helps maintain biodiversity by preventing toxic contamination of
aquatic ecosystems.

## Slide 9: Water Recycling
and Reuse
Treated wastewater can be used for irrigation, industrial processes, and groundwater recharge.
Helps address water scarcity in drought-prone regions

## Slide 10: Energy and Resource Recovery
1.
.
Advanced treatment processes recover energy (biogas) and
nutrients (phosphorus, nitrogen) from sewage
  Anaerobic digestion of sludge produces methane, which can be
used for electricity generation

## Slide 11
Wastewater treatment is essential for protecting human health, maintaining environmental balance, and promoting sustainable water management. As urbanization and industrialization increase, investment in advanced wastewater treatment technologies and policies will be crucial for a cleaner and healthier future

## Slide 12: Types of aerobic and anaerobic systems used to treat wastewater include
:
ACTIVATED SLUDGE
FIXED BED BIOREACTORS
MOVING BED BIOREACTORS
MEMBRANE BIOREACTORS
BIOLOGICAL TRICKLING FILTERS
Upflow Anaerobic Sludge Blanket (UASB) Reactor
Expanded Bed Process /ABR
The EGSB reactor -Expanded Granular Sludge Bed
Fixed Dome Anaerobic digesters (BIOGAS SEWAGE TREATMENT PLANT - IWTS

## Slide 13: THE BIOGAS TECHNOLOGY
SUSTAINABLE WASTEWATER TREATMENT
TECHNOLOGY
Will treat all the wastewater generated to satisfactory environmental standard
Clean water produced can be used for other domestic purposes and landscaping
Biogas for cooking and power generation.
This is what we do with organic waste using IWTS/AASTP

## Slide 15
info@elfadconcept.com

## Slide 16
32amp BREAKER/
CONTROL PANEL
E. C
F. B
P.U
S.T
S.P
L.S
I. C
D. D
FLOW CHART
ELFAD CONCEPT LTD
Shop D248, Ikota shopping complex, VGC, Lekki Ajah Express, Lagos.
08037217936, 07082866677.
info@elfadconcept.co m www.elfadconcept.co m
CLIENT
PREMIER HOTEL.
LOCATION
IBADAN.
JOB TITLE
ANAEROBIC AEROBIC
SEWAGE TREATMENT PLANT (AASTP)
DRAWN BY
V. A
SHEET NO.
02
DESIGNED BY M.I
CHECKED BY
ENGR. F. O. E
DATE
JANUARY 2026
LEGEND
I. C
D.D
E.C
F.B
P.U
S.T
L.S LIFT STATION
INLET CHAMBER
DOME
DIGESTER
EXPANSION
CHAMBER INLET CHAMBER
POLISHING
UNIT STORAGE
TANK
S.P
SPRINKLER SYSTEM

## Slide 17: PLAN VIEW
SECTIONAL VIEW
LIFT STATION , INLET CHAMBER
NGL
CHECKED BY
DATE
V. A.
JOB TITLE
ANAEROBIC AEROBIC SEWAGE TREATMENT PLANT (AASTP)
DRAWN BY
DESIGNED BY
M.I
ENGR. F. O. E
SHEET NO.
03
ELFAD CONCEPT LTD
Shop D248, Ikota shopping complex, VGC, Lekki Ajah Express, Lagos.
08037217936, 07082866677.
info@elfadconcept.com
www.elfadconcept.com
INLETC HAMB ER
JANUARY, 2026
CLIENT
PREMIER HOTEL.
LOCATION
IBADAN.
NGL
LIFT STATION
LIFT STATION
2500
1200
2000
200
200
150 1000 150
1000
1000
INLET CHAMBER
600
INLET CHAMBER
600

## Slide 18: PLAN VIEW
EXPANSION CHAMBER
SECTIONAL VIEW
NGL
NGL
EXPANSION CHAMBERS
CHECKED BY
DATE
JOB TITLE
ANAEROBIC AEROBIC SEWAGE TREATMENT PLANT (AASTP)
DRAWN BY V. A.
DESIGNED BY
M.I
ENGR. F. O. E
SHEET NO.
04
ELFAD CONCEPT LTD
Shop D248, Ikota shopping complex,
VGC, Lekki Ajah Express, Lagos. 08037217936, 07082866677.
info@elfadconcept.com
www.elfadconcept.com
DOME DIGESTER
DOME DIGESTERS
70CUM
70CUM
70CUM 70CUM
140CUM SEWAGE TREATMENT PLANT (BIOGAS SYSTEM)
JANUARY, 2026
DOME DIGESTER
CLIENT
PREMIER HOTEL.
LOCATION
IBADAN.

## Slide 19
PLAN VIEW
FILTRATION BED
SECTIONAL VIEW
140CUM SEWAGE TREATMENT PLANT (BIOGAS SYSTEM)
NGL
NGL
FILTRATION BED
CHECKED BY
DATE
JOB TITLE
ANAEROBIC AEROBIC SEWAGE TREATMENT PLANT (AASTP)
DRAWN BY V. A.
DESIGNED BY
M.I
ENGR. F. O. E
SHEET NO.
05
ELFAD CONCEPT LTD
Shop D248, Ikota shopping complex, VGC, Lekki Ajah Express, Lagos.
08037217936, 07082866677.
info@elfadconcept.com www.elfadconcept.com
NUTRIENT REMOVERS
NUTRIENT REMOVERS
POLISHING UNIT
CHLORINE FEEDER
CHLORINE FEEDER
JANUARY, 2026
1600
SPRINKLER SYSTEM
SPRINKLER SYSTEM
STORAGE TANK
STORAGE TANK
POLISHING UNIT
GREEN AREA
1200
4200
1200
6900
CLIENT
PREMIER HOTEL.
LOCATION
IBADAN.

## Slide 20: The Construction Process For IWTS
Excavation for Main Digester
Cast digester base/ brick wall foundation
Digester brick works
Cast reinforced concrete weak ring
Internal and external rendering digesters
Back fill outer digester area to weak ring
Cast expansion chamber foundation

## Slide 21: The Construction Process
Expansion chamber brick work
Excavation for baffle reactor and inspection chamber
Foundation baffle reactor
Block work baffle reactor and inspection chamber
Internal and external rendering baffle reactor and inspection chamber
Formwork baffle reactor cover slab, Back filling entire workspace
Integration and commissioning
Demobilization

## Slide 22: The Construction Process

## Slide 23: The Construction Process

## Slide 24: Some Projects

## Slide 25: The Effluent Biofiltration Bed and Biogas Storage

## Slide 26: Biogas from Human Feces used for Cooking

## Slide 27: SAMPLES OF INFFLUENT AND ELFAD ORGANIC TREATED EFFLUENT

## Slide 28: RRR BENEFITS REPURPOSE AND REUSE OF SPACE

## Slide 29: RRR BENEFITS REPURPOSE AND REUSE OF SPACE

## Slide 30: 8UNIT DUPLEXES AT IKATE, LEKKI

## Slide 31
3 Badaru Str., OffAdegokeStr, Masha, Surulere, Lagos. E-mail: elfadconcept@yahoo.com

## Slide 32
Central BSTP 260 cb.m at Landmark Event Center . Oniru, Lagos

## Slide 34: RRR BENEFITS
REPURPOSE AND REUSE OF SPACE
THE DOMES / AASTP/ IWTS IS UNDER THE DRIVEWAY

## Slide 35
20FT & 40FT CONTAINER LOADED WITH PARKED ON THE DOME DIGESTERS.THIS SHOW THE
STRENGTH AND STABILITY OF THE DOME DIGESTER

## Slide 40: DOMESTIC IWTS RRR BENEFITS REPURPOSE AND REUSE OF SPACE

## Slide 43: DOMESTIC IWTS SPACE RECLAMED RRR BENEFITS REPURPOSE AND REUSE OF SPACE

## Slide 44: RRR BENEFITS REPURPOSE AND REUSE OF BIOGAS FROM HUMAN FECES

## Slide 45: RRR BENEFITS REPURPOSE AND REUSE OF BIOGAS FROM HUMAN FECES

## Slide 54
SN | DESCRIPTION | EBEANO IKEJA | EBEANO CHEVRON | REMARKS
1 | TYPE OF SEWAGE | ORGANIC WASTE STRONG/ HIGH FEACAL MATTER | ORGANIC WASTE VERY STRONG/ MORE URINE/FUILD | 
2 | INFLUENT BOD | 5770 | 1491 | STRONG SEWAGE
3 | EFFLUENT BOD | 1 | 5 | < 10 MEETS REQUIREMENT
4 | INFLUENT COD | 8362 | 2194 | STRONG SEWAGE
5 | EFFLUENT COD | 8 | 32 | < 30 MEETS REQUIREMENT
6 | INF. DISOLVED OXYGEN | 0.3 | 0.1 | OK
7 | EFF. DISOLVED OXYGEN | 6.2 | 3.5 | > 2 OK
8 | INF. NITRATE-NITROGEN | 0.45 | 0.68 | OK
9 | EFF. NITRATE-NITROGEN | 4.10. | 0.02 | <5 OK
10 | INF. AMMONIA NITROGEN | 507 | 319 | 
11 | EFF. AMMONIA NITROGEN | 6.3 | 45.9 | <2 89% TREATMENT HOWEVER NOK
12 | FEACAL COLIFORM | NIL | NIL | OK
13 | CHLORINATION | 2.13 | 0.2 | OK
14 | BLOWER | YES | YES | AS SEEN IN DO RESULT
15 | PERCENTAGE TREATMENT | 99.04 | 95 | OK

## Slide 56: WHY CIRCULAR ECONOMY?
A circular economy reframes Wastewater as a valuable resource stream, rather than an environmental liability. Through recovery technologies, sludge can be converted into energy, nutrient-rich compost, soil conditioners, and treated water suitable for reuse.
These products open new economic opportunities while improving environmental sustainability.
BENEFITS
Converts waste into valuable products (energy, fertilizer, treated water)
Reduces environmental pollution and carbon emissions
Supports long-term sustainability and resource efficiency
Creates economic opportunities and local industries
Strengthens resilience of sanitation systems
Encourages innovation and technology adoption

## Slide 57: CIRCULAR ECONOMY OPPORTUNITIES IN WASTEWATER MANAGEMENT
The circular economy opens new pathways for transforming Wastewater from a liability into an economic asset. By integrating resource-recovery technologies across the sanitation value chain, cities can unlock sustainable benefits.
Key Opportunities:
Anaerobic digestion for biogas
Composting and co-composting for soil conditioners
Nutrient recovery for agriculture
Thermal treatment for energy conversion

## Slide 58: CIRCULAR ECONOMY FRAMEWORK FOR WASTEWATER MANAGEMENT
sanitation systems designed for resource recovery,
valorization technologies, digitalized waste logistics, and
market development. This approach ensures that outputs such as biogas, fertilizers, and treated water are
efficiently captured, safely managed, and commercially viable.
A circular Wastewater management system transforms waste into valuable resources through four integrated
pillars:
Resource Recovery-Oriented Sanitation Systems
Onsite and decentralized treatment units are designed to maximize recovery efficiency. These include:
Anaerobic biodigesters (fixed dome, plug-flow,
hybrid anaerobic–aerobic)
Upflow Anaerobic Sludge Blanket (UASB) reactors
MBBR-based decentralized wastewater treatment systems (DEWATS)
Anaerobic baffled reactors
Vermifiltration and compost-based systems
These systems are engineered so that biogas, digestate, and reclaimed water can be safely used or upgraded into higher-value products.

## Slide 59: CIRCULAR ECONOMY FRAMEWORK FOR WASTEWATER MANAGEMENT
Circular Waste Logistics and
Digitalization
GPS tracking of desludging trucks for accountability
Smart monitoring of septic
tanks and digesters
Digital permit management for
operators
QR-coded sludge disposal receipts to prevent illegal dumping
Valorization Technologies for Wastewater Energy
Recovery
Biogas from anaerobic digestion (60–70% methane)
Upgrading biogas to biomethane for cooking or gas grids
Co-digestion with organic waste to increase
methane yield
Black soldier fly larvae processing to produce biodiesel and protein feed
Nutrient Recovery:
Composting for NPK-rich fertilizers
Ammonia stripping for nitrogen fertilizers
Thermophilic drying to produce sanitized
organic pellets
Water Reuse:
Tertiary treatment (filtration, UV, constructed wetlands) for urban landscaping, irrigation, and industrial cooling
Market Development and Commercialization
Markets must exist for biofertilizers, pelletized soil conditioners, biogas, and biosolids.
Government intervention can stimulate demand and ensure standards.
Successful commercialization ensures that recovered resources generate economic as well as environmental value.

## Slide 60: POLICY AND REGULATORY NEEDS
Clear national guidelines for sludge treatment and reuse
Standards for energy products, compost, and effluent quality
Licensing frameworks for private-sector participation
Monitoring indicators for facility performance
Incentives for circular-economy investment and innovation
Access to Green Finance
  Climate funds (GEF, GCF, SEFA, AfDB climate financing).
    Green bonds and sustainability-linked loans.
Preferential lending rates for circular production.
Tax Incentives & Subsidies
  Reduced VAT for recycled products.
Tax breaks on equipment for recycling, renewable energy, or biogas systems.
  Import-duty waivers on green technologies and materials

## Slide 61: FINANCING MODELS FOR CIRCULAR Wastewater MANAGEMENT
Public–Private Partnerships (PPP)
  Build–Operate–Transfer (BOT): Private firm builds and operates Wastewater treatment plants, then transfers ownership to government
  Design–Build–Operate (DBO): Private partner designs, builds, and runs the system under
government oversight
  Concession-based desludging: Operators manage collection and treatment under long- term contracts
Output-Based Financing
  Payments tied to verifiable treatment volumes or resource recovery outputs
  Incentivizes efficiency and compliance with environmental standards
Carbon Finance
  Generate Certified Emission Reductions (CERs) from methane capture or compost replacing synthetic fertilizers
  Sell carbon credits to global markets to offset operational costs
Community & Estate-Level Financing
  Gated communities, markets, and estates use sinking funds or service charges for regular desludging and treatment
  Encourages local ownership and sustainability

## Slide 62: CASE STUDIES AND GLOBAL BEST PRACTICES
Dakar, Senegal
Wastewater treatment plants operating under PPP
Digital tracking of trucks
Successful marketing of fecal compost.
Kampala, Uganda
Co-treatment of Wastewater and organic waste
Biogas-to-power systems generating electricity
Bengaluru, India
Decentralized DEWATS
Water reuse for landscaping and industry

## Slide 63
THE COPENHAGEN STORY
On waste / circular economy: through its Circular Copenhagen effort, the city targeted high recycling rates, increased reuse, and CO₂ reductions from waste/resource management.
Results so far: between 2005 and 2011, Copenhagen cut CO₂ emissions by about 21%.
More recently, per-capita CO₂ emissions dropped: from ~ 4.7 tonnes CO₂e per person in 2010 to ~ 1.3 tonnes CO₂e in 2022 — and projections aim for under 1.0 t per person by 2025.
The city has dramatically increased its renewable energy supply and shifted heating systems to carbon-neutral sources (biomass + renewables) — transforming its energy infrastructure to support green goals.

## Slide 64: IMPLEMENTATION ROADMAP FOR STAKEHOLDERS
Short Term (0–2 years)
Develop circular sanitation policies
Map Wastewater flows
Establish desludging regulations
Pilot decentralized biodigester and DEWATS units
Medium Term (2–5 years)
Build regional Wastewater treatment plants
Standardize resource recovery products
Launch digital monitoring platforms
Incentivize private sector participation
Long Term (5–10 years)
Integrate sanitation into circular city masterplans
Scale up energy and fertilizer markets
Achieve 70–90% Wastewater resource recovery
Introduce reclaimed water reuse programs

## Slide 65: SAMPLES OF INFFLUENT AND ELFAD ORGANIC TREATED EFFLUENT

## Slide 70: CONCLUSION
Circular economy strategies offer the private sector and governments in west Africa a robust pathway to modernize sanitation, reduce environmental impact, enhance public health, and unlock new energy and agricultural markets. By adopting integrated policies, investing in decentralized treatment system such as IWTS(hybrid biodigesters) and promoting resource recovery innovations, our countries can transition from linear waste disposal to regenerative and financially sustainable Wastewater ecosystems. Successful implementation requires strong regulatory frameworks, public–private partnerships, and data-driven governance.

## Slide 71: TEN COMMANMENT
“Waste is not the end of a cycle; it is the beginning of a new value chain.”
“A sustainable city is one that transforms its Wastewater from a public burden into a circular resource.”
“Circular sanitation is not just about managing waste—it is about recovering energy, nutrients, and dignity.”
“Every liter of wastewater holds the potential to power homes, enrich soils, and protect the environment—if we choose circularity.”
“In a circular economy, sanitation becomes an engine of opportunity, not a cost of development.”
“Wastewater becomes a threat only when we waste its value.”
“The future of sanitation is not disposal—it is regeneration.”
“Sustainability begins when society stops throwing away resources disguised as waste.”
“Circular Wastewater management turns yesterday’s pollution into tomorrow’s solution.”
“A nation that closes its sanitation loop opens the door to clean water, clean energy, and resilient communities.”

## Slide 72: REFERENCES
Argentina Biogas Project, Global Methane Initiative (GMI).
Gold, M., Ddiba, D., “Resource Recovery from Waste,”
Stockholm Environment Institute.
Strande, L., Ronteltap, M., Brdjanovic, D. (2014). Wastewater Management: Systems Approach for Implementation and Operation. IWA Publishing.
Tilley, E., Ulrich, L., Lüthi, C., Reymond, P., & Zurbrügg, C. (2018). Compendium of Sanitation Systems and Technologies. EAWAG.
UNEP Circularity Report (2021).
WHO/UNICEF Joint Monitoring Programme (JMP),
“Progress on Household Sanitation,” 2023.
World Bank (2020). Faecal Sludge Management in Urban Areas.

## Slide 73
THANK YOU
www.elfadconcepts.com